## Slide 1: Control of Mobile Robots
Raspberry Pi Edition

## Slide 2: Introduction
Robot Models: Two-wheel Differential Drive, Omni-drive
  Computing Motor Control
  Kinematics
Demonstration

## Slide 3: Robot Model 1 Two Wheel Differential Drive
Given information about robot
  R -> radius of each wheel
  L -> length of wheelbase
Inputs
  v -> velocity
  ω -> heading
Desired information:
  Velocity of left wheel
  Velocity of right wheel

## Slide 4: Robot Model 1 Two Wheel Differential Drive
Wheel Outputs:
  vr = (2v + ωL) / 2R
  vl = (2v - ωL) / 2R
Where is the robot now, based on the measurements of the wheels

## Slide 5: Robot Model 2 Omni-drive
Inputs
  v -> velocity
  ω -> heading
Desired information: Velocity of each wheel
Calculation
  Input vector = [v * cos(ω), v * sin(ω)]
  Rotate input vector 45 degrees
    Dot multiply vector times rotation matrix of 45 degrees
  X of input vector is velocity for wheels 1 & 3
  Y of input vector is velocity for wheels 2 & 4
Example: https://www.instagram.com/p/BYxLeTlh8R6/?taken-by=zachallen417

## Slide 6: Demonstration